【２】 Movement of ONE CYCLE

| Position | Movement | Condition |
| --- | --- | --- |
| ① | Home Position | 1. Right Press (Cutter Upper) is at the Lowest position． |  |
|  |  | 2. Slide Table & Band Guide are at the Far Front position. |
|  |  | 3. Right Bandway is closing (with 2-3mm aperture) |
|  |  | 4. Arrow on BR1 points Upward (↑±45°) |
|  |  | 5. Home position Mark and Cam Follower are facing each other. |
|  |  | 6. LS1 and LS2 are OFF. |  |
|  | Start | Switch ON (It will be a reset movement if LS1 and LS2 are not OFF position). |
|  |  | 1. Cam Shaft starts rotate when BR1 if OFF and CL1 is ON. |
| ② | Reverse | 1. Right Bandway aligns strapping. |  |
|  | Preparation | 2. Right Press goes up and hold strapping. |  |
|  |  | 3. Band Guide and Right Bandway move to open position. |  |
|  |  | 4. Left Press starts to move. |  |
| ③ | Reverse | LS1 goes OFF (First OFF). |  |
|  |  | 1. Cam Shaft stops （CL1 OFF，BR1 ON） |  |
|  |  | Reverse starts （SOL1 ON） Tension Motor goes ON |  |
|  |  | 4. LS5（Reverse Pulse） catches Pulse. |  |
|  | Tensioning | →Reverse stops （SOL1 OFF） Final Tensioning starts (SOL2 ON) 6. T3 (Tension Timer) goes off. 7. Cam Shaft starts rotate again. （CL1 ON，BR1 OFF） |  |
| ④ |  | 1. Left Press holds strap. |  |
|  |  | 2. Heater Plate starts to move | ※LS1, 2 go off at the hole position. |
| ⑤ |  | LS1 goes OFF (2nd OFF). | （Rear Operation Panel is ON;LED lamp lights） |
|  |  | 1. SOL2 goes off to cut strap. |  |
| ⑥ | Cut Strap | 1. Cut strap. |  |
|  |  | 2. Primary Press → Heater goes back → Secondary Press (Sealing) |
| ⑦ | Sealing | LS1 goes OFF (3rd OFF) |  |
|  |  | 1. Cam Shaft stops if VR2 is set on. Bypassed when VR2 is at “0”, maximum 0.5 seconds |
| ⑧ |  | 1. 2nd Joint press (Sealing completes) |  |
|  |  | 2. Three presses go down and Slide Table moves back.. Release strap |
|  |  | 3. Slide Table & Band Guide go back to Home Position. |  |
| ⑨ | Automatic Strap Ejection | LS3 detects the end of strap, goes ON LS1 goes OFF Slide Table goes back Cam Shaft stops Ejection of Left over strap inside Pool box |  |
|  |  | Note: The above function works when LS3 is ON. |
| ⑩ | Forwarding | LS1 goes OFF (4th OFF) 1. Forwarding by SOL3 is OFF. |
| ⑪ | Home Position | 1. LS1 & LS2 go OFF and stop Cam Shaft. （CL1 OFF，BR1 ON） |
|  |  | Forwarding finishes by SOL3 go OFF/T2 Timer is up Complete ONE CYCLE |  |

⑫	MODE Switch (Rotary Dip Switch) 〔Fig. 22〕

・	Mode Switch is a Rotary Dip Switch at the bottom of Control Box.

・	Mode Switch is to adjust Tension Stroke of T3, and is for various arch sizes for T1 and T2.

* Note:  Turn off the Power when changing Mode Switch.

(Adjusted value is effective when power is turned on again.)

| Dip Switch No. | 0 | 1 | A | 3 | 4 | 9 |
| --- | --- | --- | --- | --- | --- | --- |
| Arch Size | S | M | M | S | S | S |
| Max. Stroke | 150 | 150 | 300 | 90 | 75 | 75 |

Arch Size	S:	W500x650H – W900x650H	Arch Circumference	2300 – 3100mm

M:	W500x650H – W1100x650H		2300 – 3500mm

7

【３】 MONITOR

《1》	 Switching to Monitor Display 〔Fig. 8〕

The face plate of Control Box changed into the Monitor Display

with the following THREE steps.

《2》	 Monitor Display

- Heater Volume caan be monitored when switching

to Monitor Display.

(Example)

1.  Set Heater Volume at 6 on a scale 〔Fig. 9〕

2.  LED Lamp lights TWELVE lamps 〔Fig. 10〕

Heater Scale shows upto 10 whereas Monitor shows 20 steps, i.e., more

precise adjustment.

②	Switching to another ADJUSTMENT　〔Fig. 11〕

Turning FR Switch       once counterclockwise swithces to another ADJUSTMENT.  Last Adjustment is VR5 (Reverse Backup/Prevention of Insufficient Reversing).  One another turn is back to Heater.

HEATER (Heater) → T1 (Cast off Volume) → T2 (Forward Timer) → T3 (Tension Timer) → VR1 (Erasure of Tension Release Noise) → VR2 (Sealing Time Adjustment) → VR3 (Heater Temperature supplement) → VR4 (Reverse Count / Prevention of Insufficient Reversing) → VR5 (Reverse Backup/Prevention of Insufficient Reversing) → HEATER (Heater)

Turning FR Switch        clockwise switches the opposite steps.

9

《2》 Improper Arrow Position

《2》	POOL TOUCH ROLLER PRESSURE AND TOUCH LEVER

①	Pool Touch Pressure Adjustment 〔Fig. 26〕

■ Decrease	Move Pool Touch Roller Spring Hook to RIGHT when using NARROW, THIN and/or SOFT Strapping.

■ Increase	Move Pool Touch Roller Spring Hook to LEFT when using WIDER, THICK and/or HARD Strapping, and Large diameter coil.

②	Touch Lever Adjustment:  Adjust without strapping between Rollers. 〔Fig. 27〕

1.  Set Stopper Bolt (HB M5x20) on Pool Shooter Bracket at Higher Position.  Shift Touch Lever to “RUN” position.

2.  Lower Stopper Bolt height until both Drive Roller and Lower Roller contact each other slightly.  And, turn the Stopper Bolt ONE turn (360 degrees) or ONE and HALF turn (540 degrees) counterclockwise and lock it with Lock Nut.

③	LS3 Adjustment 〔Fig. 28〕

Loosen fixing Bolts of LS3 Bracket.

LS3 is OFF when Strapping is IN between both Drive Roller and Lower Roller.

LS3 is ON when Strapping is OUT from both Rollers.

*  Do not push Switch Lever too much (it might damage LS3).

④	When Pool Touch Roller Pressure adjustments are required

a.●Phenomenon	 	Thin strap jams at Pool Shooter Out, which cause Pool Error (A-Limit) flashes or M2 Pool Motor stops with Error lamp flashes.

◎Adjustment   Lower the Pool Touch Roller pressure and bring the Stopper bolt of Pool Shooter Bracket.

ｂ．	●Phenomenon  Pool motor runs, but no strap fed into the Pool box

◎Adjustment   Increase the Pool Touch Roller pressure.

ｃ．	●Phenomenon  Frequent insufficient reversing on narrow strap.

・ Insufficient reversing by the nipping or jamming during forwarding strap.

・ The strap is caught at FR Roller and Feed Upper Roller.

○Cause			Deformation of strap with Pool Drive Roller and Lower Roller.

◎Adjustment	Lower the Pool Touch Roller Pressure and re-adjust the Stopper Bolt to lower the damage on the strap.

ｄ．	●Phenomenon	Pool Motor does not run and Error Lamp flashes although LS4 is ON.

○Cause 1	Overload of Pool Motor.  Excess Pool Touch Roller Pressure or Stopper Bolt is not functioning.

◎Adjustment 1	Re-adjust Pool Touch Pressure and Stopper Bolt position.

○Cause 2	Low voltage because of excess length of power cord.

◎Adjustment 2	Change into larger capacity cord.

【３】 FEED ROLLER PRESSURE ADJUSTMENT

《１》 Strap Feeding Mechanism

Adjust WITHOUT strapping

■Pre/Post Feeding →	SOL3 is ON.  Creating a Gap between Feed Upper Roller and FR Roller.  Standard Gap is approx. 1 – 1.5mm.

■ During Feeding 	→	SOL3 is OFF.  Feed Upper Roller and FR Roller touch due to the Feed Spring pressure.

- Adjustment of  Feed Upper Roller [Fig.29]

  - To increase the pressure

Loosen Lock Nut ① and turn Adjust Bolt ② counterclockwise.

(Tighten Feed Spring ③)

  - To increase the pressure                           Lock Nut         Feed Spring Adjuster

Turn Adjust Bolt ② clockwise.

(Loosen Feed Spring ③).

[Fig.29]                                                             SOL3

SOL1

15

《3》	Adjustment of Gap of Feed Upper Roller

・When  Gap is Large, Stroke of SOL3 becomes Longer.

■	GAP Adjustment can be done with FR Solenoid Ass’y positioning.

Standard Gap is 1 – 1.5mm.

a. Decrease Gap      　→　Adjust FR Solenoid Ass’y Position to the Right.

Stroke Length of SOL3 becomes shorter.

b. Increase Gap      　 →　Adjust FR Solenoid Ass’y Position to the Left.

Stroke Length of SOL3 becomes longer.

《4》	Feed Rollers Pressure Adjustments are required when;

- Strap is not secured on the package when machine operated continuously.

- Short Feed Troubles happen frequently due to poor quality.

- Feeding is not steady after machine is sitting idle for a long period of time.

ADJSUTMENT:  Increase the Pressure of Feed Rollers.

- Change of strap used:  Width, thickness and/or Manufacturer.  Especially if a portion of strap pops out from Arch track after changing strap to narrower type.

ADJSUTMENT:  Decrease the Pressure of Feed Rollers.

16

【4】 ADJUSTMENT OF REVERSE ROLLERS PRESSURE

《1》	Reverse Mechanism

■ When not reversing →	SOL1 is OFF and Reverse Upper Roller and Reverse FR Roller are not touching each other.  This Opening “C” can be adjusted by SOL1 Plunger Stopper.

STANDARD: C = 10mm 〔Fig. 31〕

■ During reversing →	SOL1 is ON and Reverse Upper Roller is pulled down by the Reverse Solenoid Ass’.Strap reverses by the pressure of Reverse Upper Roller and FR Roller (Reverse).  STANDARD: D = 0.5 – 1mm (without strap).  If D is less than the clearance, there will be no touch pressure even pulling the stroke end of SOL1 〔Fig.32〕.

《2》	When adjustments are required.

Increase pressure when;

・Strap does not wrap around package.

・Strap only comes out of the first corner of arch track, but not from second – fourth corner.

・Package surface have strong friction such as Styrofirm or Rubber, etc.

Decrease pressure when;

・Pressure is too strong such that SOL1 can not move the full length if its stroke.

《3》	Reverse Rollers Pressure STANDARD 〔Fig. 33, 34〕

Strap is pulled with force which is created by Reverse Rollers about 24.5 – 29.4N (2.5 – 3Kgf) (Direct Tension Value).

However, the STANDARD of Reverse Roller Pressure is subsitituteed with the pulling force (F) by Reverse Upper Shaft Lever during the reversing cycle (with 15.5mm strap; N=14.7 – 15.7N (1.5 – 1.6Kgf).

It can be measured in a simple manner.  Tie strap tip around a Spring Scale and turn        Feed/Reverse Switchto Reverse.  And, read the force on the Scale.

《4》	Adjustment of Reverse Rollers Pressure

①Reverse Rollers Pressure 〔Fig. 35〕

- Increase; Increase pressure on Reverse Spring.

Pull pin out and turn Reverse Spring Adjuster clockwise, direction (a).

- Decrease pressure on Reverse Spring.

Pull pin out and turn Reverse Spring Adjuster counterclockwise, direction (b).

Replace PIN after Adjustment.

② Adjustment of SOL1 and Reverse Solenoid Joint Ass’y. 〔Fig. 35〕

■Adjust SOL1 position at FR Solenoid Base.

* Push SOL1 Plunger UP by Finger (not Link Plate), then: 〔Fig. 35〕

■ When Strap is not in between Rverse Rollers →	D = 0.5 – 1mm 〔Fig. 32〕

■ When Strao is in between Reverse Rollers 	→	D = 1 – 2mm 〔Fig. 32〕

【5】 TENSION ROLLERS PRESSURE

《1》	When adjustments are required.

a.	●Phenomenon	No Tensioning even Tension Roller turns and Tension Dial is set at more than 1.

○Cause	Tension Roller and Touch Roller are apart other even the SOL2 Plunger is at its Stroke end.

b.	●Phenomenon	No Tensioning or Tension is not sufficient as Touch pressure is not enough.

○Cause 1 	Sol2 Plunger does not reach to its stroke end even Tension Roller and Touch Roller contact each other.

○Cause 2			Excess pressure on Tension Roller by Touch Roller when SOL2 Plunger is at its stroke end.

《2》	STANDARD of Tension Rollers Pressure. 〔Fir. 36〕

①	When pushing the SOL2 Plunger all the way up (without strapping), then;

* Do not push the Touch Roller Arm.

②	Adjust Tension Solenoid Adjuster to make NO clearance between Tension Roller and Touch Roller and lock it with Lock Nut.  At this point, confirm the following.

a.  Tension Roller and Touch Roller contact each other.

b.  Either Roller cannot rotate without resistance.

c.  Touch Roller and Band Guide Plate (Left Rear) do not touch.  If it contact, adjust with Adjsut bolts of Band Guide Plate.  The clearance is approx. 0.3mm.  Also, the clearance between Band Guide Plate (Left Rear) and FR Roller should be approx. 0.2mm.

d.  SOL2 Plunger is at its stroke end.

《3》	Clearance between Touch Roller and Tension Roller.

①	STANDARD 〔Fig. 37〕

Adjust the clearance by turning Stopper.

| Strap Size | Clearance |
| --- | --- |
| Standard (9 – 15.5mm) | Approx. 2mm |
| Less than 6mm | Approx. 1mm |

21

【6】 HEATER PLATE

《1》	Height Adjustment 〔Fig. 38〕

・	Adjust Heater Holder Position to get proper Heater Height using the Heater Holder Fix Screws.

・	The Gap between upper surface of Heater Plate and bottom of Slide Table is approx. 1.7mm  when Heater Plate moves under the Slide Table.

- Recommended to use the Thickness Gauge for the adjustment.

Thickness Gauge t = 1.7 mm

《2》	Right and Left Adjustment

・	Adjust Heater Arm by using Heater Arm Fix Screws. 〔Fig. 39〕

・	The Gap between Heater Plate and RH. Press is approx. 0.5mm 〔Fig. 40〕

22

【7】 REVERSE UPPER ROLLER STOPPER

《1》	STANDARD

・	The Gap between FR Roller (Reverse) and Reverse Upper Rolller is approx. 0.1mm without strap.

《2》	Adjustment of Stopper 〔Fig. 42〕

①	Loosen Lock Nut of Stopper Bolt and lower until FR Roller (Reverse) and Reverse Upper Rolller contact each other.

②	Raise Stopper Bolt until it touches FR Upper Roller Shaft to release Reverse Upper Roller.  And, turn Stopper Bolt further 90 degrees (1/4 turn).

③	Lock Stopper Bolt with Lock Nut.

【8】 RIGHT BANDWAY

- Height Adjustment

a. Adjust Right Bandway Rail to achieve proper height 〔Fig. 43〕

・Notched Section of Right Frame and Inferior surface

of Right Bandway Rail should be leveled. 〔Fig. 44-1〕

b.  Adjustment of Right Bandway Bracket.

・Adjust Right Bandway Bracket vertically in order to make Right Bandway horizontal position. 〔Fig. 44-2〕

9 – 15.5mm → Edges of Right Bandway Arm and Right Bandway Bracket meet each other.

- 6mm→ Edge of Right Bandway Bracket is 1mm above the edge of Right Bandway Arm.

・Strap reaches at the tip of Right Bandway, but does not go further.

Right Bandway is too HIGH → Strap hits Slide Table.

Right Bandway is too LOW  → Strap hits Right Block

《2》	Right and Left Adjustment

Turn Fix Screw on Right Bandway Joint to adjust Right Bandway Right and Left. 〔Fig. 45〕

【9】 SEALING ALIGNMENT 〔Fig. 46〕

①	Remove Heater Cover and Slide Table.  And, check the alignment of Right/Left Band Guide and Band Stop Guide according the datum of Slide Table Support..

②	Turn Armature section (refer P.16 [Fig. 24]) of BR1 (Sealing Brake) 360 degrees clockwise from Home Position.  And, confirm Strap is pushed against to Band Guide Right firmly.

③	Without strapping, there should be no Gap at the tip of Right Bandway and Band Guide, Right.

【10】 BRAKE BR1 AND CLUTCHES CL1 〔Fig. 48〕

Note:  Turn off the power before adjustment.

《1》	Sealing Brake BR1

①	STANDARD:	Gap between Coil and Armature is appro. 0.2 - 0.25mm.

②	Time to adjust:	Gap exceeds 0.4mm

③	ADJUSTMENT:	Loosen Armature set screws and adjust to 0.2 – 0.25mm with Thickness Gauge.  And, readjust Home Position. (Refer to “HOME POSITION”)

《2》	Sealing Clutch CL1

①	STANDARD:	Gap between Coil and Armature is approx. 0.2 - 0.25mm.

②	Time to adjust:	Gap exceeds 0.4mm

③	ADJSUTMENT:	Take V-Belt out from Motor Pulley.  Also, take Micro Belt out from the FR Drive Pulley. Loosen HBS M6x15.  Set the Shim, and adjust the clearance. Tighten HBS M6x15.

Note:  Make sure Set Screws sit on the flat points on the shaft.  Keep Set Screws in the holes. Fig. 48

7. TROUBLE SHOOTING of LIMIT SWITCH

●Phenomenon 1	Sealing Unit runs continuously by pushing Start switch.  Does not stop, No Frowarding/Reversing.

○Cause 1			Mulfunction of LS1/Poor contact/LS1 Harness is faulty.  No Input of LS1 OFF signal (LS1 is Close contact).

●Phenomenon2-1	Sealing Unit runs once by pushing Start Switch.  It seemingly shows normal movement, but stops at the timing of Forwarding Cycle.

●Phenomenon2-2	Sealing Unit is stopped along cycle.  Reset function does not work with Start Switch.  And, Sealingunit stops at each holes of Timing Plate.

○Cause 2	Mulfunction of LS2/Poor contact/LS2 Harness is faulty.  No Input of LS2 OFF signal (LS2 is Close contact).

◎Measure	Turn Power ON while Stop Switch is locked.  Bring a piece of Metal to LS1 and/or LS2, and check LED Indicator 〔Fig. 50〕 of Control Box.  Replace LS1 and/or LS2 when evaluation is faulty.

Note:  Proximity Switch LS1 and LS2 might be faulty even LED Indicator shows No error.

(Disassemble LS1 for easier check as LED Lamp of switch is difficult to check)

| LS1 | LED of LS1, LS2 | LED of Control Box | Evaluation |
| --- | --- | --- | --- |
| ON | Red Light | NO Light | Normal |
| ON | Red Light | Light | Limit Sw Normal, but malfunction of Connector / Harness |
| ON | NO Light | Light | Malfunction of Limit Sw / Connector / Harness |

・Disassemble LS1 for easier check as LED Lamp of switch is difficult to check.

・Possible to check by switching LS1 and LS2.

１0．REPLACEMENT

- Replacement of IC Box

    - Turn off the Power Switch.

    - Remove Rear Panel and Transformer Cover.

    - Remover Control Box Cover.

    - Disconnect the Harness from the IC Box.

    - Remover the fixing bolts of IC Box.  And, take IC Box out from the machine.

    - Set the Volumes and Dip Switch of New IC Box as the old IC Box. (Refer Page 7.)

Fix the new IC Box and connect the Harness.

31

【2】 REPLACEMENT OF CUTTER LOWER 〔Fig. 65〕

* Turn Power OFF and wait about 15minutes to cool down the Heater sufficiently.

①	(Reverse Strap, Push Stop Switch) Turn Power OFF.

②	Remove Upper Table Front/Rear.

③	Remove Heater Cover and Slide Table.

④	Remove Band Guide.

⑤	Turn Armature of BR1 counterclockwise until Center Press (Cutter Lower) is raised to the Cuuter Upper.  Disassemble Cutter Lower.

⑥	Assemble New Cutter Lower temporarily.

⑦	Plase 0.2mm Shim or Thickness Gauge between Right Press and Center Press.

⑧	Fix bolts little by little while pushing Cutter Lower against Cutter Upper evenly.

*  Tighten the bolt (Heater side) first.  This way, Cutter Lower will be fix evenly with Cutter Upper.

⑨	Remove Shim of ⑦.

⑩	Fix all parts and return Cam Shaft to Home Position.

【3】 REPLACEMENT OF CUTTER UPPER

* Turn Power OFF and wait about 15minutes to cool down the Heater sufficiently.

* Handle with care the Cutter Upper.

Replacement of Cutter Upper is done after Disassebling Three Block Arms.

《1》	Disassemble of Three Block Arms 〔Fig. 66〕

①	(Reverse Strap, Push Stop Switch) Turn Power OFF.

②	Remove Upper Table Front/Rear.

③	Remove Heater Cover, Slide Table and Band Guide.

④	Remove all three Block Tension Springs.

⑤	Loosen Set Bolt (HSS) of Right Arm Ass’y and pull out Arm Shaft from Left Frame.

⑥	First remove Left Arm Ass’y.  Then, take Center and Right Blocks off together.

⑦	Take Cutter Tension Spring off.

《2》	Replacement Cutter Upper 〔Fig. 67〕

①	Set Right Block Arm Ass’y onto Press Replacement Jig or Vise.  Note:  Do not damage Bearing when using Vise.

②	Fix the Ass’y bith bolt.

③	Use HBS, M5x50 Bolt and Hammer to pull out Spring Pin.  Replace Cutter Upper.

*  Same procedure for Center and Left Arm Ass’y.

④	Fix Cutter Upper with Spring Pin and take Block off.

*  Note:  Pay attention on Direction GAP of Spring Pin.  Also, Spring Pin should not be out from Block.

《3》	Assembly

①	Assemble Ctter Tension Spring first.  Then, Right and Center Arm Ass’y together back to the Frame.

②	Place Left Arm Asss’y and Arm Shaft.  Level Shaft End and Side Frame, and fix Set Bolts of Right Arm Ass’y.

③	Hook Block Tension Springs.

④	Fix Band Guide and Heater Cover.

⑤	Fix Slide Table (Refer P.33 Slide Table)

【7】 REPLACEMENT OF FEED SHOOTER ASSEMBLY

①	Remove Right Bandway Ass’y by removing HBS, M4x8 Bolts 〔Fig. 79〕.

②	Remove Gand Guide Plate (Front) 〔Fig. 79〕

③	Remove Snap Pin NO. 16 of connecting Reverse Spring Adjuster and Reverse Upper Shaft Lever, and turn Lever to left 〔Fig. 79〕.

④	Remove Right Bandway Spring 〔Fig. 79〕

⑤	Remove Right Banway Rail and Right Bandway Stopper.

⑥	Replace Feed Shooter Assembly （Refer P. 43 Strap Size Conversion）.

⑦	Adjust the Stopper of Reverse Upper Roller.

【8】 REPLACEMENT OF TENSION ROLLER

- Remove the Wing Nut and Ban Guide Plate (Front), Fig. 80.

- Remove the center bolt of End Plate, HBS M6x15, Fig. 80.

②	Set both Left and Right holes with HBS M5x12, Fig. 81.

③	Set HBS M8x25 bolt at the center hole, Fig. 81.

④	While tightening M8 bolt, the Tension Roller is pushed back, Fig. 82.

⑤	Set a new Tension Roller with facing the Key and into the Gear shaft.

- Placing the Band Guide Plate completes the replacement.

- Note that a new Tension Roller has some slimy dust on the surface.  Take them out by applying some strapping operation.

# Text boxes

⑤ Remove the RH Bandway Rail and RH Bandway Stopper

Shaft

BR1

Gear Mission

Timing Plate

Fixing Bolt

FR Drive Pulley

Tension Drive Pulley

Fig. 8

Fig. 9

Fig. 10

Fig. 11

Fig. 32

Approx 8mm

Without strap

D = 0.5 – 1mm

With strap

D = 1 – 2mm

Approx 33mm

Without strap

D = 5 – 1mm

With strap

D = 1 – 2mm

Approx 11mm

Approx. 30mm

Spring Pin

<Strap Size 5, 6mm>

Spring Pin

<Strap Size 9 – 15.5mm>

Reverse Release Spring

14

Fig. 28

Limit Switch Bracket

11

Feed Trouble (Short Feed)

Because RH Bandway moves forward at the time of feeding.

Home Position

Arrow stops at ±４５°from the vertical line.

#### Late

19

Fixing Bolt

Thickness Gauge

Fig. 33

Fig. 34

〔Fig. 35〕

〔Fig. 36〕

Fig. 37

Fig. 82

HBS M8x25

39

① Remove RH Bandway Ass’y

34

〔Fig. 67〕

Direction of Chasm

Spring Pin

Tightener

Vice for Press Arm

Arm

Attachement for RQ-8

〔Fig. 66〕

Left Frame

Left Arm Ass’y

Center Arm Ass’y

Cutter Tension Spring

Block Tension Spring

Set Screw HSS

Right Arm Ass’y

Right Frame

Armature

26

17

33

Arm Shaft

〔Fig 65〕

Right Press Arm

Center Press Arm

Cutter Lower

Cutter Upper

Put a Screw Driver, and forced to open two blocks.

Place a Shim in between

32

Fix Slide Table Screw (Heater Side) temporarily

LED lamp of LS1

〔Fig. 50〕

27

Normal Close

〔View “A”〕

〔Fig. 46〕

RH Bandway

Heater Side

Right Bandway

Datum Line

Datum Line

Band Guide Left

Datum Line

④ Remove the RH Bandway Spring

Datum Line

Fig. 31

FR Drive Pulley

HSS M6x12

1) Turn the Main Sw

2) Push the Stop Sw

3) Press the Reset Sw for 1 second.

LED Lamp

F/R Sw

Stopper

Reverse Solenoid Link Plate

Lock Nut

13

##### Fig. 26

Stronger

Fix at 1/3 position

Softer

Drive Roller

Lower

Lower Roller

Incomplete Reversing

Because LH Gripper goes up too high while reversing

Slide Table Support

Band Guide Right

View “A”

Band Stop Guide

Adjustment for Strap Aignment

25

#### Standard

Early

#### Symptoms

#### RH Bandway Can & Cam Follower

#### Band Guide does not stop at Home Position

Strap becomes loose after tensioning because SOL2 Solenoid has released before LH Gripper hold strap.

IC Box

Rotary Dip Switch

Band Guide Right

Datum Line

There should be no opening.

〔Fig. 45〕

Lock Nut

Lock Nut

Fixing Bolt

Fixing Bolt

RH Bandway Joint

RH Bandway Joint

24

〔View “B”〕〔Fig. 44-2〕

〔View “A”〕〔Fig. 44-1〕

RH Bandway Arm

Place exactly at the position

9mm    White

5-6mm  Black

Right Frame

RH Bandway Rail

Leveled

RH Bandway Bracket

〔Fig. 43〕

RH Bandway Bracket

RH Bandway Rail

〔Fig. 42〕

Reverse Upper Roller

Feed Shooter Ass’y

Lock Nut

Stopper Bolt

FR Roller

(Reverse Side)

23

FR Upper Roller Shaft

Fixing Bolts for Limit Sw bracket

Touch Lever Position

Fig. 27

Stopper Bolt HB M5x20

3

2

Slide Table

Slide Table

Thickness Gauge

Heater Arm

Heater Terminal

0.5mm Clearance

Heater

18

〔図-８１〕

There are slot holes for adjustment (Set around at the center).

There are slot holes for adjustment (Set around at the center).

Feed Upper Roller

Clearance 1 – 1.5mm

FR Roller

Fig. 80

20

20

Fig. 38

Reverse Spring

Reverse Spring Adjuster

Reverse Solenoid Joint Assembly

Snap Pin

Link Plate

FR Solenoid Base

Adjust Bolts for SOL 1

Do not push the Link Plate.  Push the Plunger

Tension Roller

No Clearance

Plunger

Lock    Adjust

Nut       Nut

No Interference

Band Guide Plate (Left Rear)

Adjust Bolt for Band Guide Plate (Left Rear)

FR Roller        Touch Roller

Clearance 	 No Interference

Approx 0.2mm	 Approx. 0.3mm

Band Guide Block, Right

Tension Roller

Touch Roller Arm

Stopper

Open clearance

HBS M5x12

SW

Tension Roller

Wing Nut

Band Guide Plate (Front)

Tension Roller End Plate

40

Fig. 79

② Remove the Band Guide Plate (Front)

③ Remove the Snap Pin