8. STRAP SIZE　9mm⇔12mm CONVERSION

【1】 ADJUSTMENT

《1》	Band Width Block 〔Fig. 51〕

Gap A Adjustment according to Datum (of Slide Table Support).

Adjust with Strap in use

Strap size 12mm or wider	A = Strap Width plus 1mm

Strap size 9mm or narrow	A = Strap Width plus 0.5mm

| Strap Width | Gap A |
| --- | --- |
| 12ｍｍ | 13ｍｍ |
| 9ｍｍ | 9.5ｍｍ |

《2》	Right Bandway 〔Fig. 53〕

Adjust by positioning of Band Adjuster.

For 12mm, set the Band Adjuster at the center of

hole.  Level the Band Adjuster with Right Bandway as

pointed with arrow mark.

For 9mm, push the Band Adjuster in.

《3》	Pool Shooter Out and Pool Shooter In Assembly 〔Fig. 54〕

Adjust with Pool Shooter Guide Out (LH) and Pool Shooter Guide In.

For 12mm, pull the Pool Shooter Guide In

and  Out.

For 9mm, push them.

Fig.54

【2】 STRAP CONVERSION KIT

| Description | 12mm Exclusive Parts | 9mm Exclusive Parts | Quantity |
| --- | --- | --- | --- |
| Metal Collar | 0890-320237 | 0890-320248 | 7 |
| Reverse Upper Roller | JK26-51-40110 | JK26-51-20110 | 1 |
| Feed Shooter | JK26-51-40130 | JK26-51-20130 | 1 |
| Pool Cover, Upper | JK26-51-40140 | JK26-51-20140 | 1 |
| Band Keeper (A) | JK26-51-40160 | JK26-51-20160 | 1 |
| Band Keeper (B) | JK26-51-40170 | JK26-51-20170 | 1 |
| Band Keeper (C) | JK26-51-40180 | JK26-51-20180 | 1 |
| Collar | JK26-51-40210 | JK26-51-20210 | 1 |
| Self-Loading Guide (B) | JK26-51-40220 | JK26-51-20220 | 1 |

【3】 POOL BOX

Fig. 55 shows the construction of Pool Box, and positioning of each parts.

- Metal Collar

- Reverse Upper Roller

- Feed Shooter

- Pool Cover Upper

- Band Keeper (A)

- Band Keeper (B)

- Band Keeper (C)

- Collar

- Self-Loading Guide (B)

Note:  The above conversion kit applies

For the following serial No.

10001058, 1000325 – 10003246.

Fig.55

30

【4】 REPLACEMENT OF BELT

*  Too tight Belt Tension damages of the Shaft center.

《2》	Micro Belt 340J & Sealing Motor V-Belt A-23, -24.

①	Remove Micro Belt 340J-3 from FR Pulley.

②	Remove Sealing Motor V-Belt A-23, -24 from Timing Motor Pulley.

③	Replace the Belt.

④	Tensioning of Belts is as follows.

■ Micro Belt 340J-3

Set Idler Bracket (A) temporarily.  Pull point “b” of HBS, M8x15 with Spring Scale horizontal direction, and fix Idler Bracket (A) when Spring Scale shows 39.2N (4Kgf).  Belt moves approx. 6mm when it is pushed by approx. 9.8N (1Kgf) of force at point “c” 〔Fig. 70〕.

■ Sealing Motor V-Belt A-23, -24

Belt moves approx. 8mm when it is pushed by approx. 9.8N (1Kgf) of force at point “d”.

35

【5】 REPLACEMENT OF ARCH FLAP SPRING SET

Replacement of Arch Flap Spring Set

①	Different Arch Flap Springs 〔Fig. 71 & 72〕

L is the length with Stad.  Dimension with (  ) shows the length setting on Arch Frame.

| Strap Size | Straight Section | 1st - 2nd Corner | 3rd - 4th Corner |
| --- | --- | --- | --- |
| 9 and 12 mm | Spring Wire Diameter | φ0.8 | φ0.8 | φ0.65 |
|  | Ｌ | 25 | 25 | 23 (25) |

Note:  Useφ0.65 Spring at Connecting section with Right Bandway Ass’y and 4th Corner of Arch.

②	Replacement

Replace when Spring is broken or slacked.

1.  Remove Arch Flaps.

2.  Remove faulty Arch Flap Spring Set from Arch Frame by turning counterclockwise 〔Fig. 73〕

3.  Using Screwdriber Bit, fix New Arch Flap Spring Set to the stud of Arch Frame 〔Fig. 73〕

4.  Set Arch Flaps along the direction of Strap Forwarding as shown in 〔Fig. 74〕.

Note:  A dimension (betweel Lock Nut to Burring section should be approx. 0.1 – 0.2mm 〔Fig 75〕

【6】 WIRE REPLACEMENT OF SELF-LOADING UNIT

①	Remove Rear Panel and Transformer Cover, and open Front Door.

②	Shaft Touch Lever from Position A to Position B. 〔Fig. 76〕.

③	Remove Hold Bolt, Nut Spring (body Rear side), and pull out Wire 〔Fig. 77〕.

④	Blow Lubricant Spray inside of Tube (Pusher Wire Set) and insert New Wire.  Insert by turning the tube if wire is caught.

⑤	Fix Wire when tip of wire comes out approx. 10mm from Hold Bolt, and return Spring 〔Fig. 77〕

- Move Touch Lever gradually from A position to B position (approx. 10mm).  Self-Loading Flaps should be closed at B position 〔Fig. 78〕

Fine Adjustment should be done with Wire Adjust Bolt.  Lock it with Nut when completed 〔Fig. 77〕

# Text boxes

Slide Table Support

Band Width Block

Fig. 51

Fig. 53

Right Bandway

Band Adjuster

Pool Shooter In Ass’y

Pool Shooter Out Ass’y

Pool Shooter Guide In

Pool Shooter Guide Out (Left)

28

Pool Shooter Guide Out Left

Pool Shooter Guide In

4th Corner

RH Bandway

PW M5

Snap Pin

Band Keeper (C)

Pool Cover Lower

Band Keeper (B)

Pool Door

Collar

Pool Cover Upper

Metal Collar

Band Keeper (A)

1st Corner

29

29

0.8mm

3rd Corner

2nd Corner

0.8mm

Straight Section

0.8mm

L length

Arch Flap Spring Set

d

c

Timing Motor Pulley

Sealing Motor Belt A-23, -24

Micro Belt 340J-3

Idler Roller Bracket (A)

b

0.65mm for the connecting with RH Bandway

RH Bandway Stand Set

36

Fix a Screw Driver HSS M4x5

Strap Flow

Screw Driver

Flap

Hook

Stud Bolt

Arch Flap Spring Set

Driver Bit (QFK-RQ-F2-00201)

〔Fig. 74〕

〔Fig. 75〕

〔Fig. 73〕

37

Spring

Wire

B

10mm

A

Tube

Fig. 78

Fig. 76

Fig. 77

Adjust Nut

When closing too quickly for the position of A.

When opening too quickly for the position of A.

Wire Adjust Bolt

Wire

Wire

Hold Bolt

More than 10mm

38